## Slide 1
K. Park, J. Kang, G. Sohn
Dept. of Earth & Space Science & Engineering, York University Toronto, M3J1P3 Canada - (kunwoo7, jkang99 ,gsohn)@yorku.ca
ULTRA-WIDEBAND-BASED RANGE-ONLY SLAM FOR UAV LOCALIZATION IN OUTDOOR ENVIRONMEMT
Background
Results of Localization
Ultra-Wideband(UWB) Based Localization
Range-Only SLAM for UAV Localization
UWB anchors
D
XW
YW
ZW
W
XS
YS
ZS
S
A precision monitoring of the status of critical infrastructure on a timely manner is critical for public safety and economics. Today’s practice for inspecting critical infrastructure mainly rely on human forces, which is time-consuming, prone to errors and often put inspectors in dangerous situations. To address these issues, Unmanned Aerial Vehicle (UAV) is recently attracting large amount of attentions as an alternative solution to human-centric labors.
However, UAV mainly relies on consumer-grade lower-quality of positioning systems and has critical drawback to operate in downtown core areas where high-rise buildings often interfere signals from Global Navigation Satellite System (GNSS).
Thus, there is high demand to increase UAV localization accuracy in GNSS-denial environments. One emerging solution is Ultra-Wideband (UWB) based localization due to its robustness to multipath and cm-level ranging error.
Nevertheless, fixed UWB modules (anchors) have to be precisely installed to achieve localization by additional surveying work which hinders quick and easy use of the UWB based localization.
In this poster, we present UWB based Range Only Simultaneous Localization and Mapping (RO-SLAM) to facilitate quick installation of anchors and achieve UAV localization simultaneously. Approximate location of the UWB anchors and the UAV are continually updated based on the Extended Kalman Filter (EKF) using distance measurements. As a result, the coordinates of the UWB anchors converge within a certain amount of error and UAV localization is performed based on the distance measurement from the anchors.
UWB Ranging Calibration
Chart: UWB Ranging Error
| 5046.8822381893788 | 10019.615452581296 | 14987.38890551338 | 20030.771549640318 | 25012.766587315244 | 29969.538757875587 | 34949.0205107441 | 40072.37189883797 | 45059.26476603264 | 50031.282449274324
 | 5024.3117 | 9998.1814 | 14963.7674 | 20007.3516 | 24991.8901 | 29952.3812 | 34965.3115 | 40049.8047 | 45037.8248 | 50002.446
Reference(x) | UWB(y) | Difference (UWB-REF)
5046.88 | 5024.31 | -22.57
10019.61 | 9998.18 | -21.43
14987.38 | 14963.76 | -23.62
20030.77 | 20007.35 | -23.41
25012.76 | 24991.89 | -20.87
29969.53 | 29952.38 | -17.15
34949.02 | 34965.31 | 16.29
40072.37 | 40049.80 | -22.56
45059.26 | 45037.82 | -21.43
50031.28 | 50002.44 | -28.83
UWB sensor measured about 21 mm longer than reference in average. This calibrated range is used for localization and SLAM algorithm.
unit: mm
EKF Model for Localization
where
Dynamic model
Prediction
Correction
(m)
(m)
: UAV position
: UAV velocity
Ground truth value
Estimated value
(X axis unit: 0.1s)
Localization Simulation Setup
0,0,1
0 ,50,1.25
50,50,2
50,0,2.5
Initial location
50,25,20
Initial velocity
0,2,0
The UAV moves along a circle with radius of 25m
at a height of 20m, at an uniform linear velocity 2m/s.
Install UWB anchors at different heights
at each vertex of 50m by 50m square.
The distance from an anchor measured every 1/10s.
Guo, K., Qiu, Z., Miao, C., Zaini, A. H., Chen, C. L., Meng, W., & Xie, L. (2016). Ultra-wideband-based localization for quadcopter navigation. Unmanned Systems, 4(01), 23-34.
Range Only SLAM
UAV position: = ,UAV velocity:=
Unknown Anchor position :=, =
(height(z) of each anchor is assumed be known)
anchor 1
anchor 2
anchor 3
anchor 4
Results of Range Only SLAM
Prediction
Correction
Ground truth value
Estimated value
, , , : Anchor coordinates
Conclusion
Acknowledgements
This project is partially supported by an NSERC (Natural Sciences and Engineering Research Council of Canada) grant in collaboration with ISW and CGQ.
UWB ranging and EKF can be used to perform UAV localization within 1 meter.
Range Only SLAM can be used to accurately estimate the position of anchor and localization of UAV.